Addendum to the Vapour Pressure Method of Moller et al.

Introduction

In 2008 an improvement of the vapour prediction method developed by Nannoolal et al. [1] was published [2]. The method aimed to extend the very good method presented by Nannoolal et al. The improvements were far reaching, introducing new structural groups, introducing size dependant groups, changing the structure of the group interactions, changing the form of the equation and extending amount of data in the training set. The result was a method which is claimed to have better performance for more compounds.

During the course of the last 2 years both methods have been put under some scrutiny by various groups around the world [xxx,xxx,xxx]. The Centre for Atmospheric Sciences in Manchester, more specifically Dr Mark Barley (who is one of the researchers there), gave quite some correspondence regards problems with the method and its implementation. The result is that some minor errors, and two substantial errors, with the method of Moller et al. have been discovered. This memorandum will outline the nature of the errors, the steps taken to correct them and the parameters accompanying the correction.

Problems with the method

One of the changes that was made to the method of Nannoolal et al. was to change the structure of the group interactions, previously the group interactions followed the following structure:

where m is number of interacting groups, n is number of heavy atoms and GI is the group interaction. This expression was introduced when fitting pure component properties (PCPs) and therefore it was theorized that since it is essentially a slope that is been fitted that this could be changed to:

Unfortunately this wasn’t given sufficient thought. While both expression perform sufficiently well for molecules with low numbers of functional groups (as are present in the training set) for large number of functional groups Eqn.  grows dramatically, leading to nonsense vapour pressure values. Consider the example of cyclohexaamylose shown in Fig. 1, it contains 30 interacting functional groups, this would cause Eqn.  to get exceptionally large (group 200 – 153 times; group 214 – 216 times and group 290 – 66 times) while Eqn.  has the denominator to damper the effect of the large number of group interactions ((m-1)xn = 1914) and therefore produce realistic numbers.

Fig. 1 Molecular formula of cyclohexaamylose.

It clear that the solution to this error is to introduce a group interaction term similar to Eqn. . In the subsequent PhD work by Moller [3], which among other things introduced a water activity method, the following group interaction scheme was found to be superior to that of Eqn. :

This expression was tested on quite a number of compounds with large numbers of functional groups and performed sufficiently well. For this reason Eqn.  has been adopted as the expression of choice for the group interaction term proposed in this memo. The updated table of model parameters is shown in Table 1. All the group values were refitted and not just the group interactions, the result is only minor changes to the group contribution values. The overall error with the new parameters is practically identical to the overall error with the old parameters and therefore no discussion of errors will be presented here (the reason for this is that the number of multifunctional compounds in the training set is quite small).

The second major error effects far fewer compounds and was simply a logical oversight. The size dependant groups for nitriles, aliphatic alcohols and aliphatic carboxylic acids are split into 2 groups, one for big and another for small. In the paper by Moller et al. [2] it was stated that the criteria for selecting which group to use is simply the number of heavy atoms (n). This is true for monofuctional groups, but for multifunctional groups the selection criteria should be nxvi where vi is the size dependant group frequency. This seems quite minor, however it introduces a jump discontinuity which is physically unrealistic. So for example succinic acid (C4H6O4) would have previously been (incorrectly) considered small ([n = 8]<9) would now be (correctly) considered large ([vixn = 16]>9).

Minor alterations

The corrections in covered in this section are not to address errors that have been found but rather to clarify some points on the method implementation and introduce some minor alterations. The first 2 alterations have to do with the coefficient of the logarithmic correction term (D’). The form of the group contribution scheme was given as follows:

Where for the OH groups there are 2 dEi values, one for the OH group contribution and one for the OH group interaction. For the group interaction term the frequency is an “on-off” type value where if there is more than one OH group then vi = 1 if not then vi = 0. This was not made clear in the original paper. A slightly modified form of Eqn.  should be used as it given superior alcohol representation (in expanded form):

where vOH is the number of OH groups, na is number of heavy (non-hydrogen) atoms; d, dEOH and dEOH-OH are the group contribution values and vOH-OH is the “on-off” group interaction frequency. The introduction of the vOH term in the denominator of the OH-OH term simply helps the group interaction term fall away faster for large number of groups.

Another alteration has to do with the aromatic carboxylic group interactions. Aromatic carboxylic acid groups (group 48) should be considered the same as the aliphatic ones (groups 53 and 155) for group interactions (i.e. 2 aromatic COOH groups will use the same group interaction term as 2 aliphatic COOH groups). This was not covered in the original paper as there were no multifunctional compounds with aromatic carboxylic groups.

Table 1 Updated parameter table for the vapour pressure method of Moller et al. (Ink No. – the number used in the fragmentation program to identify the group, Size Dep – group values with yes need to be multiplied by the number of heavy atoms in the molecule, Size dependant group constants always have a frequency of 1, Prty – the order in which groups are fragmented – lower numbers first, * - group value only fitted to 1 compound, ** - group value only fitted to 2 compounds)

| Ink No | Name | Description | dBi | Example | Prty | Size Dep | Ref No |
| --- | --- | --- | --- | --- | --- | --- | --- |
| - | A | The constant term A | 9.47970 | - | - | - | - |
| Aliphatic carbon groups |  |  |  |  |  |
| 1 | -CH3 | Methyl group attached to a non-aromatic non-electronegative atom | -0.03206 | 2,2-Dimethylbutane | 135 | No | 101 |
| 4 | -CH2- | CH2 in a chain | 0.07558 | n-Butane | 141 | No | 102 |
| 5 | >CH- | CH in a chain | 0.10049 | 3-Ethylpentane | 144 | No | 103 |
| 6 | >C< | C in a chain | 0.01643 | 2,2,4-Trimethylpentane | 146 | No | 104 |
| 2 | -CH3 | Methyl group attached to a non-aromatic electronegative atom | 0.12260 | N-Methylaniline | 132 | No | 105 |
| 7 | -CH2- | CH2 in a chain attached to an electronegative atom | 0.13265 | Ethylenediamine | 136 | No | 106 |
| 8 | -CH< | CH in a chain attached to an electronegative atom | 0.13629 | 5-Ethyl-2-nonanol | 137 | No | 107 |
| 9 | >C< | C in a chain attached to an electronegative atom | -0.02810 | tert-Butanol | 138 | No | 108 |
| 29 | -CH3 | Methyl group attached to a ring carbon | -0.10527 | Methylcyclohexane | 122 | No | 109 |
| 10 | -CH2- | CH2 in a ring | -0.02275 | Cyclohexane | 143 | No | 110 |
| 11 | >CH- | CH in a ring | 0.07517 | Methylcyclohexane | 145 | No | 111 |
| 12 | >C< | C in a ring | 0.15009 | 1,1-Dimethylcyclopentane | 147 | No | 112 |
| 131 | >CH(r) - C(r)< | CH in a ring bonded to a Carbon in a different ring | 0.01164 | cis-Decahydronaphthalene | 110 | No | 113 |
| 136 | C(k)-C(r)-3C(r) | Ring carbon attached to 3 other ring carbons and a chain carbon | 0.03314 | 1,3-Dimethyl adamantane | 108 | No | 114 |
| 137 | C-4C(r) | Ring carbon attached to 4 other ring carbons | 0.17291 | Spiro[4.5]decane | 109 | No | 115 |
| 24 | -CH2(r)-en | CH2 in a ring attached to an electronegative carbon | 0.08216 | 1,4-Dioxane | 142 | No | 116 |
| 14 | >CH- | CH in a ring attached to an electronegative atom | 0.13765 | Cyclopentanol | 139 | No | 117 |
| 15 | >C< | C in a ring attached to an electronegative atom | -0.07267 | Perfluorocyclopentane | 140 | No | 118 |
| 139 | C(r)_3C(r)_en | Ring Carbon bonded to 3 other ring carbons and an en atom | -0.00851 | 1-Nitroadamantane | 107 | No | 119 |
| 26 | CH2= | Double bonded carbon at the end of a chain/ring | -0.00815 | 1-Nonene | 117 | Yes | 120 |
| 20 | -CH=C- | Double bonded carbon in a chain with only 1 carbon neighbour | 0.00313 | 2-Heptene | 121 | Yes | 121 |
| 27 | -C=C- | Double bonded carbon in a chain with 2 carbon neighbours | 0.00711 | 2-Methyl-2-pentene | 118 | Yes | 122 |
| 31 | >C=C=C< | C=C=C; cummulated double bonds | 0.08052 | 1,2-Butadiene | 112 | Yes | 123 |
| 33 | >C=C-C=C< | C=C-C=C (chain); conjugated double bonds (chain) | 0.04120 | trans-1,3-Pentadiene | 114 | Yes | 124 |
| 21 | >C=C< | Double bond between carbons in a ring | 0.00168 | 1,3-Cyclopentadiene | 123 | Yes | 125 |
| 13 | -C=C< | Double bonded carbon in a ring with 2 carbon neighbours | 0.02864 | 1-Methylcyclohexene | 120 | Yes | 126 |
| 32 | >C=C-C=C< | C=C-C=C (ring); conjugated double bonds (ring) | -0.00190 | 1,3-Cyclopentadiene | 113 | Yes | 127 |
| 134 | >C(r)=C(k) | Carbon in a ring double bonded to a carbon outside the chain | 0.01669 | beta-Pinene | 106 | Yes | 128 |
| 25 | CH# | Carbon triple bonded to another carbon at the end of a chain | -0.04184 | 1-Octyne | 124 | Yes | 129 |
| 22 | -CtC- | Triple bond between 2 carbons in a chain | -0.01393 | 2-Heptyne | 125 | Yes | 130 |
| 34 | -C#C-C#C- | C#C-C#C; conjugated triple bonds | 0.00991** | 2,4-Hexadiyne | 111 | Yes | 131 |
| Aromatic carbon groups |  |  |  |  |  |
| 3 | -CH3 | Methyl group attached to an aromatic atom | -0.03718 | 1-Methyl naphthalene | 133 | No | 201 |
| 16 | -CH(a)< | CH in an aromatic ring | 0.00691 | Benzene | 128 | No | 202 |
| 17 | >C(a)< | C in an aromatic ring | 0.13222 | Propylbenzene | 131 | No | 203 |
| 19 | =C(a)< | Aromatic carbon attached to three aromatic neighbours | -0.00328 | Naphthalene | 116 | No | 204 |
| 132 | C(a)-C(r) < | Aromatic carbon bonded to a carbon in a ring | 0.08205 | 1,2,3,4-Tetrahydronaphthalene | 129 | No | 205 |
| 133 | C(a)-C(a) | 2 Aromatic carbons chain bonded | 0.15828 | Benzidine | 130 | No | 206 |
| 135 | C(a)-r-C(a) | Aromatic carbon bonded to an aromatic carbon in a ring | -0.10077 | 9H-Fluorene | 115 | No | 207 |
| 138 | C(a)-C= | Aromatic carbon attached to a double bonded carbon | 0.27831 | Divinylbenzene | 127 | No | 208 |
| 18 | >C(a)< | C in an aromatic ring attached to an electronegative atom | 0.24600 | Aniline | 119 | No | 209 |
| Fluorine groups |  |  |  |  |  |  |
| 35 | F- | Fluorine attached to nonaromatic carbon | 0.01909 | 1-Fluoropentane | 92 | No | 301 |
| 38 | F-C-1Halo | Flourine attached to a carbon with one other halogen atom | 0.07450 | Perfluorocyclopentane | 71 | No | 302 |
| 39 | F-C-2Halo | Flourine attached to a carbon with two other halogen atoms | 0.06602 | 1,1,1,2-Tetrachloro-2,2-difluoroethane [R112a] | 70 | No | 303 |
| 36 | F-C= | Fluorine attached to double bonded carbon | 0.07029 | 2-Fluoropropane | 69 | No | 304 |
| 148 | F-C=(1 Halo) | Flourine attached to a double bonded carbon with one other halogen atom | 0.05489 | 1,1-Difluoroethene | 68 | No | 305 |
| 37 | F-C(a) | Fluorine attached to aromatic carbon | -0.11552 | Fluorobenzene | 91 | No | 306 |
| 116 | Fe-Si< | Flourine attached to a silicon atom | 0.18079 | Silicon tetrafluoride | 1 | No | 307 |
| Chlorine groups |  |  |  |  |  |  |
| 40 | Cl- | Chlorine attached to noaromatic carbon | 0.02294 | Chloroethane | 76 | No | 401 |
| 43 | Cl-C-1Halo | Chlorine attached to a carbon with one other halogen atom | -0.00101 | 2-Bromo-2-chloro-1,1,1-trifluoroethane | 67 | No | 402 |
| 44 | Cl-C-2Halo | Chlorine attached to a carbon with two other halogen atoms | 0.02263 | 1,1,1-Trichloroethane [R140a] | 66 | No | 403 |
| 42 | Cl-C= | Chlorine attached to double bonded carbon | 0.05474 | 2-Chloro-1,3-butadiene | 65 | No | 404 |
| 149 | Cl-C=(1 Halo) | Chlorine attached to a double bonded carbon with one othe halogen atom | 0.10733 | Tetrachloroethylene | 64 | No | 405 |
| 41 | Cl-C(a) | Chlorine attached to aromatic carbon | -0.24456 | Chlorobenzene | 77 | No | 406 |
| 117 | Cl-Si< | Chlorine attached to a silicon atom | -0.04326 | Trichlorosilane | 2 | No | 407 |
| 113 | COCl- | Acid Chloride | 0.30163 | Trichloroacetyl chloride | 19 | No | 408 |
| Bromine groups |  |  |  |  |  |  |
| 45 | Br- | Bromine attached to nonaromatic carbon | -0.06190 | 1,2-Dibromoethane | 78 | No | 501 |
| 144 | Br-C-1Halo | Bromine attached to a Carbon with one other halogen atom | 0.03436 | 2-Bromo-2-chloro-1,1,1-trifluoroethane | 75 | No | 502 |
| 145 | Br-C-2Halo | Bromine attached to a Carbon with two other halogen atom | -0.06034 | Tribromomethane [R20B3] | 74 | No | 503 |
| 146 | Br-C= | Bromine attached to a double bonded carbon | 0.12369 | Vinyl bromide | 73 | No | 504 |
| 46 | Br-C(a) | Bromine attached to aromatic carbon | -0.23289 | Bromobenzene | 79 | No | 506 |
| 118 | Br-Si< | Bromine attached to a silicon atom | -0.16653 | Silicon tetrabromide | 3 | No | 507 |
| Iodine groups |  |  |  |  |  |  |
| 47 | I- | Iodine attached to carbon | -0.01350 | Ethyl iodide | 61 | No | 601 |
| 119 | I-Si< | Iodine attached to a silicon atom | 1.27845** | Triiodomethylsilane | 4 | No | 607 |
| Oxygen groups |  |  |  |  |  |  |
| 53 | -COOH (n=<9) | COOH Group attached to a small molecule (n =< 9) | 0.81213 | Pentanoic acid | 25 | Yes | 701 |
| 155 | -COOH (n>9) | COOH Group attached to a large molecule (n > 9) | 0.08306 | Dodecanoic acid |  | Yes | 702 |
| 48 | C(a)-COOH | Aromatic COOH | 2.35370* | Benzoic acid | 24 | No | 703 |
| 49 | -OH (n=<4) | OH Group attached to a small molecule (n =< 4) | -0.32187 | Ethanol | 93 | Yes | 704 |
| 153 | -OH (n>4) | OH Group attached to a large molecule (n > 4) | -0.04853 | 5-Ethyl-2-nonanol |  | Yes | 705 |
| 50 | C(a)-OH | Aromatic OH | 0.68415 | 2-Naphthol | 94 | No | 706 |
| 51 | -O- | Ether oxygen | 0.10973 | Diethyl ether | 96 | No | 707 |
| 52 | -O- | Aromatic oxygen | 0.21686 | Furan | 95 | No | 708 |
| 54 | -COO - | Ester in a chain | 0.52436 | 1,3-Benzenedicarboxylic acid dimethyl ester | 26 | No | 709 |
| 55 | -COO - | Formic acid ester | 0.50096 | Formic acid ethyl ester | 28 | No | 710 |
| 56 | -COO - | Ester in a ring (lactone) | 0.49674 | gamma-Butyrolactone | 27 | No | 711 |
| 57 | >C=O | Ketone bonded to aromatic ring | 0.11377 | Acetophenone | 58 | No | 712 |
| 58 | >C=O | Ketone | -0.03413 | Acetone | 59 | Yes | 713 |
| 59 | -CHO | Aldehyde in Chain | 0.35027 | Acetaldehyde | 57 | No | 714 |
| 60 | -CHO | Aldehyde attached to an aromatic ring | 0.25675 | Benzaldehyde | 56 | No | 715 |
| 61 | O=C(-O-)2 | Carbonate diester | 0.49248 | Carbonic acid dimethyl ester | 15 | No | 716 |
| 62 | -CO-O-CO- | Anhydrides | 0.79979 | Acetic anhydride | 10 | No | 717 |
| 63 | -CO-O-CO- | Cyclic anhydrides with double or aromatic bond | 0.92784 | Maleic anhydride | 9 | No | 718 |
| 64 | >(OC2)< | Epoxide | -0.05484 | Ethylene oxide | 54 | Yes | 719 |
| 65 | -O-O- | Peroxides | 1.72030* | Di-tert.butyl peroxide | 34 | No | 720 |
| 66 | -OCOO- | Carbonates O-C=O & -O | 0.49696 | Propylene carbonate | 36 | No | 721 |
| 67 | >C=O | Carbonyl(C=O) with S attached to Carbon | -0.27172* | Methyl thioacetate | 42 | No | 722 |
| 68 | >C=O | Urea | 0.40287 | 1,1,3,3-Tetramethyl urea | 7 | No | 723 |
| 69 | -OCON< | Carbamate | 3.64989* | Methyldimethylcarbamate | 6 | No | 724 |
| Nitrogen groups |  |  |  |  |  |  |
| 70 | -CONH< | Amide with no substituents | 2.13114* | Acetamide | 29 | No | 801 |
| 71 | -CONH< | Amide with one substituent attached to the nitrogen | 1.54292 | N-Methylformamide | 11 | No | 802 |
| 72 | -CONH< | Amide with two substituents attached to the nitrogen | 0.45925 | N,N-Dimethylformamide (DMF) | 12 | No | 803 |
| 73 | OCN- | Isocyanate | 0.19590 | Isocyanic acid methyl ester | 31 | Yes | 804 |
| 141 | -OCN(a) | IsoCyanate attached to an aromatic carbon | 0.45450 | Phenyl isocyanate | 30 | No | 805 |
| 74 | ONC- | Oxime | 2.54770 | Methyl ethyl ketoxime | 32 | No | 806 |
| 75 | NO2- | Nitro group attached to a nonaromatic carbon | 0.29689 | Nitromethane | 21 | No | 807 |
| 76 | NO2- | Nitro group attached to an aromatic carbon | 0.15037 | Nitrobenzene | 22 | No | 808 |
| 77 | NO2- | Nitrite | -0.32857** | Ethyl nitrite | 23 | No | 809 |
| 78 | -ON= | Isoxazole O-N=C | 0.50042* | 5-Methyl-4-nitroisoxazole | 51 | No | 810 |
| 79 | NO3- | Nitrate | 0.79232 | Ethylnitrate | 14 | No | 811 |
| 80 | NH2- | Primary amine attached to nonaromatic carbon/silicon | -0.05227 | Ethylenediamine | 98 | Yes | 812 |
| 81 | NH2- | Primary amine attached to aromatic carbon | 0.29860 | Aniline | 97 | No | 813 |
| 82 | -NH- | Secondary amines (chain) attached to carbons/silicons | 0.38441 | Dibutylamine | 102 | No | 814 |
| 86 | =N- | Secondary amines (chain) attached to one carbons/silicons via double bond | 0.82002 | N-Benzylidenemethyl amine | 105 | No | 815 |
| 93 | -NH- | Secondary amines (ring) attached to carbons/silicons | 0.54934 | Morpholine | 101 | No | 816 |
| 94 | -NH- | secondary amines attached to aromatic carbons/silicons | 0.27388 | N-Methylaniline | 33 | No | 817 |
| 84 | -N< | Tertiary amine attached to carbons/silicons | -0.22854 | N,N-dimethylaniline | 104 | No | 818 |
| 92 | -N< | tertiary amines attached to aromatic carbon | 0.05020 | N,N-Dimethylaniline | 43 | No | 819 |
| 85 | >N< | Nitrogen attached to four carbons | -1.16781* | N,N,N',N'-Tetramethylmethylenediamine | 35 | No | 820 |
| 140 | C2-N-C(r) | Cyclic Tertiary Amines | -0.29163 | N-Methylpiperidine | 103 | No | 820 |
| 83 | N=N | Azene N=N | -0.02889 | Azobenzene | 50 | No | 821 |
| 130 | >N-N< | A hydrazine functional group | 0.93778 | Hydrazine | 49 | No | 822 |
| 143 | N-N_C | Hydrazine with 1 carbon neighbours | 0.69585 | Phenylhydrazine | 48 | No | 823 |
| 142 | N-N_C2 | Hydrazine with 2 carbon neighbours | -0.14041 | 1,1-Dimethylhydrazine | 47 | No | 824 |
| 87 | =N- | Aromatic nitrogen in a five-membered ring | 0.73215 | Oxazole | 100 | No | 825 |
| 88 | =N- | Aromatic nitrogen in a six-membered ring | 0.25193 | 2-Methylpyridine | 99 | No | 826 |
| 89 | -CtN (n=<12) | CN Group attached to a small molecule (n =< 12) | -0.04392 | Acetonitrile | 60 | Yes | 827 |
| 154 | -C#N (n>12) | CN Group attached to a large molecule (n>12) | 0.07874 | Tetradecanenitrile |  | Yes | 828 |
| Sulfur groups |  |  |  |  |  |  |
| 98 | -S-S- | Disulfide | 0.00689 | Dimethyl disulfide | 55 | No | 902 |
| 99 | -SH | Thiol or mercaptane attached to carbon | -0.00787 | 1-Propanethiol | 80 | No | 903 |
| 100 | -S- | Thioether | -0.06540 | Ethyl methyl sulfide | 81 | No | 904 |
| 101 | -S- | Aromatic thioether | -0.13637 | Thiazole | 82 | No | 905 |
| 102 | -SO2- | Sulfolane O=S=O | -0.37725* | 2,4-Dimethylsulfolane | 18 | No | 906 |
| 104 | -SO2N< | Sulfon amides, attached to N and to S with 2 double bond O | 0.17994 | N,N-Dimethyl-methanesulfonamide | 38 | No | 908 |
| 105 | >S=O | Sulfoxide | 0.52729* | Dimethyl sulfoxide | 40 | No | 909 |
| 106 | SCN- | Isothiocyanat | 0.01696 | Allyl isothiocyanate | 20 | No | 910 |
| 107 | >SO3 | Sulfate with one oxygen replaced by another atom | 0.43352* | Benzenesulfonic acid,ethyl ester | 39 | No | 911 |
| Phosphorous groups |  |  |  |  |  |  |
| 95 | P(O)O3- | Phosphate triester | 0.65259 | Methyl diphenyl phosphate | 8 | No | 1001 |
| 96 | >P< | Phosphine | -0.04561 | Triphenylphosphine | 46 | No | 1002 |
| 97 | PO3- | Phosphite attached to only 3 Oxygens,PO3 | -0.15853* | Triethoxyphosphine | 45 | No | 1003 |
| Metal groups |  |  |  |  |  |  |
| 108 | >Se< | Selenium | 0.48426** | Diselenide, diphenyl | 52 | No | 1101 |
| 109 | AsCl2- | Arsenic dichloride attached to a carbon | 0.33997 | Methylarsenic dichloride | 17 | No | 1102 |
| 110 | >Sn< | Stannane with four carbon neighbors | 0.13794 | Tetramethylstannane | 62 | No | 1103 |
| 111 | B(O-)3 | Boric acid triester | 0.46251 | Boric acid trimethyl ester | 16 | No | 1104 |
| Germanium groups |  |  |  |  |  |  |
| 114 | GeCl3- | GeCl3 attached to carbon | 0.23913 | Trichlorosilyl(trichlorogermyl)methane | 13 | No | 1201 |
| 115 | >Ge< | Germane with four carbon neighbors | 0.40216 | Tetramethylgermane | 63 | No | 1202 |
| Silicon groups |  |  |  |  |  |  |
| 120 | -SiH3 | Silane Group | -0.27218 | Butylsilane | 84 | No | 1301 |
| 121 | -SiH2- | Primary Silicon Group | 0.27766 | Trisilane | 88 | No | 1302 |
| 122 | -SiH< | Secondary Silicon Group | -0.27220 | Triethylsilane | 89 | No | 1303 |
| 123 | >Si< | Tertiary Silicon Group | 0.09298 | Tetraethylsilane | 90 | No | 1304 |
| 124 | -SiH3 | Silane Group attached to an elecromagnetic atom | 0.18974 | Monochlorosilane | 83 | No | 1305 |
| 127 | SiH2 | SiH2 attached to electronegative atoms | 0.21806 | Dichlorosilane | 85 | No | 1306 |
| 128 | SiH | SiH attached to electronegative atoms | 0.03309 | Trichlorosilane | 86 | No | 1307 |
| 125 | >Si< | Silicon Atoms bonded to elecromagnetic atoms | 0.11733 | Tetrachlorosilane | 87 | No | 1308 |
| 129 | CH3-Si | Methyl group attached to a Silicon atom | -0.03374 | Tetramethylsilane | 134 | No | 1309 |
| Special groups |  |  |  |  |  |  |
| 150 | no H | No hydrogen atoms | -0.19495 | Perfluoropentane |  | No | 1401 |
| 151 | one H | one Hydrogen atom | -0.04827 | 2-Bromo-2-chloro-1,1,1-trifluoroethane |  | No | 1402 |
| Size dependant group constants |  |  |  |  |  |
| 170 |  | Alkenes group constant | -0.03682 |  |  | No | 2001 |
| 171 |  | Alkynes group constant | 0.58091 |  |  | No | 2002 |
| 172 |  | Ketone group constant | 0.71842 |  |  | No | 2003 |
| 173 |  | Epoxy group constant | 0.70573 |  |  | No | 2004 |
| 174 |  | IsoCyanate group constant | -0.45738 |  |  | No | 2005 |
| 175 |  | Short OH group constant (n=<4) | 6.27492 |  |  | No | 2006 |
| 176 |  | Long OH group constant (n>4) | 5.24404 |  |  | No | 2007 |
| 177 |  | Primary amine group constant | 0.84041 |  |  | No | 2008 |
| 179 |  | Short CN group constant (n=<12) | 0.56132 |  |  | No | 2010 |
| 180 |  | Long CN group constant (n>12) | -1.04824 |  |  | No | 2011 |
| 181 |  | Short COOH group constant (n=<9) | -2.57882 |  |  | No | 2012 |
| 182 |  | Long COOH group constant (n>9) | 3.92182 |  |  | No | 2013 |
| Group interactions |  |  |  |  |  |  |
| 200 |  | Alcohol - Alcohol Interaction | -4.71956 |  |  | No | 3001 |
| 201 |  | Alcohol - 1 Amime Interaction | -3.88115 |  |  | No | 3002 |
| 202 |  | Alcohol - 2 Amine Interaction | -8.95373 |  |  | No | 3003 |
| 203 |  | Alcohol - Thiol Interaction | -10.16458* |  |  | No | 3004 |
| 205 |  | Alcohol - Ether Interaction | -14.35895 |  |  | No | 3006 |
| 207 |  | Alcohol - Ester Interaction | -20.46935 |  |  | No | 3008 |
| 208 |  | Alcohol - Ketone Interaction | -20.17369** |  |  | No | 3009 |
| 210 |  | Alcohol - Cyan Interaction | 1.28492* |  |  | No | 3011 |
| 220 |  | 1 Amime - 1 Amime Interaction | 10.17517 |  |  | No | 3021 |
| 221 |  | 1 Amime - 2 Amine Interaction | -2.35759** |  |  | No | 3022 |
| 224 |  | 1 Amime - Ether Interaction | 4.87158 |  |  | No | 3025 |
| 226 |  | 1 Amime - Ester Interaction | -17.71899* |  |  | No | 3027 |
| 230 |  | 1 Amime - Aromatic O Interaction | -10.30558* |  |  | No | 3031 |
| 232 |  | 1 Amime - Alcohol (a) Interaction | 33.03490* |  |  | No | 3033 |
| 237 |  | 1 Amime - Nitro(a) Interaction | 5.60601 |  |  | No | 3038 |
| 239 |  | 2 Amine - 2 Amine Interaction | -2.61666** |  |  | No | 3040 |
| 242 |  | 2 Amine - Ether Interaction | -0.38331* |  |  | No | 3043 |
| 257 |  | Thiol - Thiol Interaction | 3.76376 |  |  | No | 3058 |
| 267 |  | Thiol - Alcohol (a) Interaction | 2.97641* |  |  | No | 3068 |
| 274 |  | Carboxy - Carboxy Interaction | -61.22494 |  |  | No | 3075 |
| 286 |  | Carboxy - Aromatic S Interaction | -50.44323* |  |  | No | 3087 |
| 290 |  | Ether - Ether Interaction | 0.39710 |  |  | No | 3091 |
| 291 |  | Ether - Epox Interaction | 11.11875 |  |  | No | 3092 |
| 292 |  | Ether - Ester Interaction | 1.12699 |  |  | No | 3093 |
| 293 |  | Ether - Ketone Interaction | -16.97401 |  |  | No | 3094 |
| 294 |  | Ether - ThioEther Interaction | -13.78509* |  |  | No | 3095 |
| 295 |  | Ether - Cyan Interaction | 1.38626 |  |  | No | 3096 |
| 298 |  | Ether - Alcohol (a) Interaction | -12.48454 |  |  | No | 3099 |
| 299 |  | Ether - Aldehyde Interaction | -2.94131 |  |  | No | 3100 |
| 303 |  | Ether - Nitro(a) Interaction | -2.64771** |  |  | No | 3104 |
| 304 |  | Ether - Iso Cyan(a) Interaction | -32.29329* |  |  | No | 3105 |
| 305 |  | Epox - Epox Interaction | -8.30210* |  |  | No | 3106 |
| 319 |  | Ester - Ester Interaction | 0.80055 |  |  | No | 3120 |
| 320 |  | Ester - Ketone Interaction | 0.00307 |  |  | No | 3121 |
| 322 |  | Ester - Cyan Interaction | 4.79222 |  |  | No | 3123 |
| 323 |  | Ester - Aromatic O Interaction | 12.27720* |  |  | No | 3124 |
| 324 |  | Ester - 6 N Ring Interaction | 34.90694** |  |  | No | 3125 |
| 325 |  | Ester - Alcohol (a) Interaction | -25.39290* |  |  | No | 3126 |
| 326 |  | Ester - Aldehyde Interaction | 1.20149* |  |  | No | 3127 |
| 332 |  | Ketone - Ketone Interaction | 0.47824 |  |  | No | 3133 |
| 334 |  | Ketone - Cyan Interaction | 12.53967* |  |  | No | 3135 |
| 344 |  | ThioEther - ThioEther Interaction | -5.49026* |  |  | No | 3145 |
| 355 |  | Cyan - Cyan Interaction | 3.87689 |  |  | No | 3156 |
| 357 |  | Cyan - 6 N Ring Interaction | 6.79035** |  |  | No | 3158 |
| 368 |  | Aromatic O - Aldehyde Interaction | 1.94212* |  |  | No | 3169 |
| 371 |  | Aromatic O - 5 N Ring Interaction | -0.78283* |  |  | No | 3172 |
| 374 |  | 6 N Ring - 6 N Ring Interaction | 1.43116 |  |  | No | 3175 |
| 375 |  | 6 N Ring - Alcohol (a) Interaction | -17.96727* |  |  | No | 3176 |
| 382 |  | Alcohol (a) - Alcohol (a) Interaction | -0.52433 |  |  | No | 3183 |
| 389 |  | Aldehyde - Aldehyde Interaction | 7.87563* |  |  | No | 3190 |
| 395 |  | Iso Cyan - Iso Cyan Interaction | -102.82720* |  |  | No | 3196 |
| 401 |  | Aromatic S - 5 N Ring Interaction | -2.84572** |  |  | No | 3202 |
| 404 |  | 5 N Ring - 5 N Ring Interaction | -21.83168* |  |  | No | 3205 |
| 407 |  | Nitro(a) - Nitro(a) Interaction | -9.95224 |  |  | No | 3208 |
| 408 |  | Nitro(a) - Iso Cyan(a) Interaction | 357.52880 |  |  | No | 3209 |

[1]	Nannoolal, Y., Rarey, J., Ramjugernath, D., Estimation of Pure Component Properties Part 3: Estimation of the Vapor Pressure of Non-Electrolyte Organic Compounds via Group Contributions and Group Interactions. Fluid Phase Equilib., 2008. 269: p. 117-133.

[2]	Moller, B., Rarey, J., Ramjugernath, D., Estimation of the Vapour Pressure of Non-Electrolyte Organic Compounds via Group Contributions and Group Interactions. J. Mol. Liq., 2008. 143: p. 52-63.

[3]	Moller, B., Activity of Complex Multifunctional Organic Compounds in Common Solvents, in Chemical Engineering. 2009, University of KwaZulu Natal: Durban.

# Comments

Componello (sp?) Barley etc. need to still find the papers